## Slide 1
GPU-Accelerated Parallelization of
Common Computer Vision Applications
Emilio Del Vecchio, Kevin Lin, Senthil S. Natarajan
Department of Electrical and Computer Engineering, Rice University
-Graphics Processing Units (GPU’s) have recently become popular for their ability to parallelize computations and achieve much greater efficiency as compared to the serial implementation of a CPU.
VS
Fig 1. The GPU’s parallel architecture allows it to parallelize massive computations.
-Our objective: utilize the GPU’s ability to accelerate computer vision applications like facial recognition, edge detection, and motion tracking.
-Due to the proliferation of computer vision in many regular tasks, this affords us an opportunity to explore how to make such common algorithms more efficient.
Reduce high frequency noise from the image with a Gaussian blur
Fig 5. FFT of grayscale noisy image, unfiltered (left) versus filtered (right)
Use the Sobel operator to approximate the gradient of the image, then determine the gradient’s magnitude and angle at each pixel
3. Classify edges by suppressing non-maximum pixels along the gradient direction with a spatial tolerance threshold
Fig 6. Original image (left), Sobel filter output (center), final edges (right)
Fig 7. Two sequential frames in a video stream and the detected difference between them
Fig 8. Spatial density map (left), motion area estimation (right)
Calculate a pixel-by-pixel difference map from the edges of two frames, applying movement tolerance thresholding in the process
Estimate the motion region from a difference density map
I. INTRODUCTION
II. FACIAL RECOGNITION
III. EDGE DETECTION
IV. MOTION DETECTION
V. GPU SPEEDUP RESULTS
VI. CONCLUSIONS
Extract HAAR features of a face from a set of positive and negative training images.
2. Use Adaptive Boosting machine learning to train a multi-stage, or cascade, classifier, against positive and negative HAAR features.
3. Apply final cascade classifier to a loaded image. The OpenCV library provides modules to encapsulate this process.
Fig 2. Example HAAR features of a random face
Fig 3. Cascade Classifier training rejects most non-face regions early.
Fig 4. Original sample image (left), detected faces (right)
-In edge detection, as the computation size becomes larger, the speedup decreases, an unexpected trend. However this could be due to the memory overhead of running multiple parallel tasks in sequence.
-Overall, the results demonstrated that GPUs offer a powerful solution to the rising data requirements of modern computational and signal processing problems.
Despite any trends or outliers, the GPU implementations consistently were faster than the CPU counterparts.
-Potential limitations include: CUDA memory optimization and usage of 3rd party libraries (especially with facial recognition).
-The NVIDIA CUDA framework was used to run the parallel implementations of our algorithms.
-The results below were obtained on a Intel Core i5 4200U CPU and an NVIDIA GeForce GTX 860M GPU.
VII. ACKNOWLEDGEMENTS
-We would like to thank CJ Barberan and Richard Baraniuk for their guidance and support in this project.
Fig 9. CUDA facial recognition (top) consistently achieved 1.1 to 5.1x speedup. CUDA edge detection (middle) achieved 5.2 – 10.3x speedup. CUDA motion tracking tracking (bottom) achieved 4.2– 9.5x speedup.