## Slide 1
GPU Acceleration of Edge-Based Motion Detection
and Facial Recognition with NVIDIA CUDA
Emilio Del Vecchio, Kevin Lin, Senthil S. Natarajan
Department of Electrical and Computer Engineering, Rice University, Houston, TX 77005
-Graphics Processing Units (GPU’s) are powerful tools for parallelized computations on large data inputs, achieving massive speedups over a serial CPU
VS
Fig 1. Massively parallel GPU architecture compared to a multicore CPU
-NVIDIA CUDA (Compute Unified Device Architecture) exposes simple C-based APIs for GPU computation
-Our objective: utilize the GPU’s ability to accelerate computer vision algorithms like facial recognition, edge detection, and motion detection
-Existing computer vision algorithms, when parallelized with CUDA, run several times faster than on a CPU
Reduce high frequency noise from the image with a Gaussian blur
Fig 5. FFT of grayscale noisy image, unfiltered (left) versus filtered (right)
Use the Sobel operator to approximate the gradient of the image, then determine the gradient’s magnitude and angle at each pixel
3. Classify edges by suppressing non-maximum pixels along the gradient direction with a spatial tolerance threshold
Fig 6. Original image (left), Sobel filter output (center), final edges (right)
Fig 7. Two sequential frames in a video stream and the detected difference between them
Fig 8. Spatial density map (left), motion area estimation (right)
Calculate a pixel-by-pixel difference map from the edges of two frames, applying movement tolerance thresholding in the process
Estimate the motion region from a difference density map
I. INTRODUCTION
II. FACIAL RECOGNITION
III. EDGE DETECTION
IV. MOTION DETECTION
V. GPU SPEEDUP RESULTS
VI. CONCLUSIONS
Extract HAAR features of a face from a set of positive and negative training images.
2. Use Adaptive Boosting machine learning to train a multi-stage, or cascade, classifier, against positive and negative HAAR features.
3. Apply final cascade classifier to a loaded image. The OpenCV library provides modules to encapsulate this process.
Fig 2. Example HAAR features of a random face
Fig 3. Cascade Classifier training rejects most non-face regions early.
Fig 4. Original sample image (left), detected faces (right)
-Generally, our algorithms demonstrated increasing speedup with pixel count because of the overhead associated with launching kernels on small input sizes.
-Deviations from this trend result from large memory footprints and lack of consideration for idle thread times.
-In all cases, GPU parallelization resulted in increased throughput, demonstrating that GPU computation is a viable and fast solution for signal processing on big data.
-We implemented our algorithms in C using the CUDA framework. The results below were obtained on a Intel Core i5 4200U CPU and an NVIDIA GeForce GTX 860M GPU.
VII. ACKNOWLEDGEMENTS
-We would like to thank CJ Barberan and Richard Baraniuk for their guidance and support in this project.
Fig 9. CUDA facial recognition (top) consistently achieved 1.1 – 5.1x speedup. CUDA edge detection (middle) achieved 5.2 – 10.3x speedup. CUDA motion detection (bottom) achieved 4.2 – 9.5x speedup.
Chart: Facial Recognition Speedup
| 4000x4000 | 3000x3000 | 2000x2000 | 1000x1000 | 500x500 | 100x100
Speedup | 5.039 | 5.117 | 5.062 | 4.077 | 2.386 | 1.11
Chart: Edge Classification (Non-Maximum Suppression and Selective Thresholding) Speedup
| 6000x6000 | 5000x5000 | 4000x4000 | 3000x3000 | 2000x2000 | 1000x1000 | 500x500
Speedup | 5.23 | 5.709 | 6.129 | 6.959 | 7.848 | 9.319 | 10.351
Chart: Motion Area Estimation (Spatial Difference Density) Speedup
| 7500x7500 | 6000x6000 | 5000x5000 | 4000x4000 | 3000x3000 | 2000x2000 | 1000x1000 | 500x500 | 100x100
Speedup | 4.265 | 8.805 | 8.678 | 9.457 | 9.548 | 8.923 | 8.9 | 7.82 | 5.085